Lab machine pinging raspberry pi
10 counts, 0.2s interval
min/avg/max/mdev = 0.588/0.660/0.712/0.036ms

Raspberry pi pinging lab machine
10 counts, 0.2s interval
min/avg/max/mdev = 0.587/0.702/0.813/0.067ms

Raspberry pi pinging lab machine
100 counts, 0.001s interval (sudo)
min/avg/max/mdev = 0.143/0.458/0.674/0.140ms

Raspberry pi pinging lab machine
10,000 counts, flooding (sudo)
Data below shows 3 different runs. Found out that not using -i will not display individual pings.
5. Raspberry Pi pinging lab machine

Initial 3 conditions
1000 measurements, intervals 0.01, 0.001 and 0.0001 respectively

The trend shows that reducing intervals results in generally faster round trips
Rerunning the test with more runs as I reduce interval time (to match total run time, I.e 10,000 runs for 0.001s interval and 100,000 runs for 0.0001s interval respectively, left and right)
Increasing the total number of runs seemed to have shifted the graph towards the left compared to the original 1000 pings (reduced round trip time on average).

When running the same test three times (1000 round trips, 0.01s interval), there seems to be quite some variance in the tests itself, as seen in the picture below where 3 of the histograms are overlayed. Each histogram is run on the same conditions (1000 pings, 0.01s interval).

When put into CDF form, the graphs below are obtained. (Side by side with histogram)

 1000 pings, 0.01s interval. Large number of pings occur with round trip timings around 0.75ms
90% of round trip timings are below 0.76ms

1000 pings, 0.001s interval. Round trip timings are mostly located around 0.675ms and 0.55ms. Overall on average it is faster than 0.01s intervals.
90% of round trip times are below 0.7ms
1000 pings, 0.0001s interval. Round trip timings is generally also skewed more towards the left than 0.001s interval.
90% of round trip times are below 0.67ms

Checking CDFs for greater ping numbers (10,000 pings 0.001s and 100,000 pings 0.0001s)

10,000 pings, 0.001s interval. 90% of round trip timings are below 0.59ms
The comparison becomes obvious when plotted together. Blue lines = 10,000 pings, brown = 1000pings.

Same trends occurs for the 0.0001s interval, when raised to 100,000 pings (Graphs above)
Comparison to 1000pings graph below, brown line = 100,000 pings. Blue ling = 1000 pings.